## Slide 1
“Mold considerations when assessing robotics requirements”
Jason Holbrook
Sales Manager
Krauss Maffei Corporation
859-653-4309
Jason.holbrook@kraussmaffei.com

## Slide 2
Speaker Bio:
Jason Holbrook, Sales Manager, Krauss Maffei Corporation:
Jason started his career with Worthington Custom Plastics following his graduation with a B.Sc. in Engineering Technology & Mgt. from Ohio University in 1995. He later joined ITW-Nifco as a Sales Engineer, managing the Toyota North America Account. In 2000 Jason joined Wittmann Battenfeld as a Regional Manager for the Mid-West. Then in 2012, Jason joined Krauss Maffei as a Sales Mgr. for Mid-West where he is presently employed today.
In his position as a Sales Manager for Krauss Maffei Jason brings with him a strong background in plastics injection machine technology and automation. His diverse experience in several key end markets including automotive, appliance, packaging, medical, & consumer, combined with 20 years of injection molding experience, provides a solid background to promote the latest in current & relevant injection molding technologies.
Insert Speaker Photo here

## Slide 3
1.) Linear or Articulated Robot?
Linear:
Pro: Typically less expensive
Pro: Faster mold harvesting
Pro: Easier to program
Con: Less articulation of the part
Con: Less useful post molding
Articulated:
Pro: multifunctional
Pro: more useful post molding (value add)
Pro: can be configured for tight spaces
Con: typically more expensive
Con: typically slower part harvesting
Con: more difficult to program

## Slide 4
1A.) Linear or Articulated Robot – or a combination of both?
Consider your wrist options
Consider: 1.) Torque, 2.) Weight, 3.) Extra Daylight
A/C Servo Combination Wrist
Opposing Pneum. Wrist Flip

## Slide 5
2A.) Linear Layout : Op-Side, Non-Op, L-Mount?
Considerations:
Minimize stroke & floor space requirements
Maximize part clearance above mold
  Always design so “Mold Close Signal” can be made without having to flip the robots wrist. Flipping wrist delays mold close – extending cycle.
Operator Side
Non-Op Side
L-Mount

## Slide 6
2B.) Articulated Layout: Floor, Shelf, or Clamp Mounting ?
Considerations:
Minimize stroke & floor space requirements
Maximize part harvesting time:
  Try to position articulated robots to allow for the fastest part harvesting and minimal mold open requirement
Maximize post molding value added processes
Floor Mount
Shelf Mount
Clamp Mount

## Slide 7
3.) Pick & Place OR Automated Cell ?
Pick & Place: Stack-Up of Tolerance Loose:
Typically has a broad allowance of tolerances
Can use robots standard position tolerance
Does not affect overall part assembly tolerance
Automated Cell: Stack-Up of Tolerance Tight:
Typically demands minimal allowance of tolerances
Should NOT rely solely on robots position tolerance
Definitely affects overall part assembly tolerance
ISOLATE Robot & IMM from stack-up of tolerances

## Slide 8
4.) Minimize vibration to maximize tolerance control
Ground vibration to the floor – just like electricity !!
Use more mass to dissipate more vibration
Isolate robot & automation from vibration when necessary

## Slide 9
5.) Poke Yoke the system when possible
Add mold coding
Add End-of-Arm Tool coding
Code End-of-Arm to Mold with 24v signal to IMM to “Goof Proof”
EOAT Coding Connector
Mold Coding Connector

## Slide 10
6.) Use Quick Change EOAT Mounting to simplify
Minimizes wear & tear on robot mounting surfaces
Standardizes vacuum & gripper mapping
Provides a safe means of hanging EOAT’s for storage
Makes for faster job changes
Dovetail Quick Change
Auto Quick Change
EOA Tool Tree Storage

## Slide 11
7.) Guarding Properly
Know your current OSHA / ANSI standard – check latest version
Must prevent physical entry unless properly interlocked
Must prevent accidental entry under normal conditions
Isle ways need Overhead Protection

## Slide 12
Questions ?

## Slide 13
Thank You!